## Slide 1: Program Optimization 15-213: Introduction to Computer Systems 10th Lecture, Oct. 1, 2015

## Slide 2: Today
Overview
Generally Useful Optimizations
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Removing unnecessary procedure calls
Optimization Blockers
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism
Dealing with Conditionals

## Slide 3: Performance Realities
There’s more to performance than asymptotic complexity
Constant factors matter too!
  Easily see 10:1 performance range depending on how code is written
  Must optimize at multiple levels:
    algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs are compiled and executed
  How modern processors + memory systems operate
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 4: Optimizing Compilers
Provide efficient mapping of program to machine
  register allocation
  code selection and ordering (scheduling)
  dead code elimination
  eliminating minor inefficiencies
Don’t (usually) improve asymptotic efficiency
  up to programmer to select best overall algorithm
  big-O savings are (often) more important than constant factors
    but constant factors also matter
Have difficulty overcoming “optimization blockers”
  potential memory aliasing
  potential procedure side-effects

## Slide 5: Limitations of Optimizing Compilers
Operate under fundamental constraint
  Must not cause any change in program behavior
    Except, possibly when program making use of nonstandard language features
  Often prevents it from making optimizations that would only affect behavior under pathological conditions.
Behavior that may be obvious to the programmer can be obfuscated by languages and coding styles
  e.g., Data ranges may be more limited than variable types suggest
Most analysis is performed only within procedures
  Whole-program analysis is too expensive in most cases
  Newer versions of GCC do interprocedural analysis within individual files
    But, not between code in different files
Most analysis is based only on static information
  Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative

## Slide 6: Generally Useful Optimizations
Optimizations that you or the compiler should do regardless of processor / compiler
Code Motion
  Reduce frequency with which computation performed
    If it will always produce same result
    Especially moving code out of loop
long j;
int ni = n*i;
for (j = 0; j < n; j++)
a[ni+j] = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 7: Compiler-Generated Code Motion (-O1)
set_row:
testq %rcx, %rcx # Test n
jle .L1 # If 0, goto done
imulq %rcx, %rdx # ni = n*i
leaq (%rdi,%rdx,8), %rdx # rowp = A + ni*8
movl $0, %eax # j = 0
.L3: # loop:
movsd (%rsi,%rax,8), %xmm0 # t = b[j]
movsd %xmm0, (%rdx,%rax,8) # M[A+ni*8 + j*8] = t
addq $1, %rax # j++
cmpq %rcx, %rax # j:n
jne .L3 # if !=, goto loop
.L1: # done:
rep ; ret
long j;
long ni = n*i;
double *rowp = a+ni;
for (j = 0; j < n; j++)
*rowp++ = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 8: Reduction in Strength
  Replace costly operation with simpler one
  Shift, add instead of multiply or divide
    16*x --> x << 4
    Utility machine dependent
    Depends on cost of multiply or divide instruction
      On Intel Nehalem, integer multiply requires 3 CPU cycles
  Recognize sequence of products
for (i = 0; i < n; i++) {
int ni = n*i;
for (j = 0; j < n; j++)
a[ni + j] = b[j];
}
int ni = 0;
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++)
a[ni + j] = b[j];
ni += n;
}

## Slide 9: Share Common Subexpressions
  Reuse portions of expressions
  GCC will do this with –O1
/* Sum neighbors of i,j */
up = val[(i-1)*n + j ];
down = val[(i+1)*n + j ];
left = val[i*n + j-1];
right = val[i*n + j+1];
sum = up + down + left + right;
long inj = i*n + j;
up = val[inj - n];
down = val[inj + n];
left = val[inj - 1];
right = val[inj + 1];
sum = up + down + left + right;
3 multiplications: i*n, (i–1)*n, (i+1)*n
1 multiplication: i*n
leaq 1(%rsi), %rax # i+1
leaq -1(%rsi), %r8 # i-1
imulq %rcx, %rsi # i*n
imulq %rcx, %rax # (i+1)*n
imulq %rcx, %r8 # (i-1)*n
addq %rdx, %rsi # i*n+j
addq %rdx, %rax # (i+1)*n+j
addq %rdx, %r8 # (i-1)*n+j
imulq %rcx, %rsi # i*n
addq %rdx, %rsi # i*n+j
movq %rsi, %rax # i*n+j
subq %rcx, %rax # i*n+j-n
leaq (%rsi,%rcx), %rcx # i*n+j+n

## Slide 10: Optimization Blocker #1: Procedure Calls
Procedure to Convert String to Lower Case
  Extracted from 213 lab submissions, Fall, 1998
void lower(char *s)
{
size_t i;
for (i = 0; i < strlen(s); i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 11: Lower Case Conversion Performance
  Time quadruples when double string length
  Quadratic performance
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower1

## Slide 12: Convert Loop To Goto Form
  strlen executed every iteration
void lower(char *s)
{
size_t i = 0;
if (i >= strlen(s))
goto done;
loop:
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
i++;
if (i < strlen(s))
goto loop;
done:
}

## Slide 13: Calling Strlen
Strlen performance
  Only way to determine length of string is to scan its entire length, looking for null character.
Overall performance, string of length N
  N calls to strlen
  Require times N, N-1, N-2, …, 1
  Overall O(N2) performance
/* My version of strlen */
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++;
length++;
}
return length;
}

## Slide 14: Improving Performance
  Move call to strlen outside of loop
  Since result does not change from one iteration to another
  Form of code motion
void lower(char *s)
{
size_t i;
size_t len = strlen(s);
for (i = 0; i < len; i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 15: Lower Case Conversion Performance
  Time doubles when double string length
  Linear performance of lower2
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower2 | 0 | 3.8e-05 | 7.7e-05 | 0.000115 | 0.000153 | 0.000191 | 0.000229 | 0.000267 | 0.000306 | 0.000344 | 0.000382 | 0.00042 | 0.000458 | 0.000497 | 0.000535 | 0.000573 | 0.000611 | 0.000649 | 0.000687 | 0.000726 | 0.000764 | 0.000802 | 0.00084 | 0.000878 | 0.000917 | 0.000955
lower1
lower2

## Slide 16: Optimization Blocker: Procedure Calls
Why couldn’t compiler move strlen out of inner loop?
  Procedure may have side effects
    Alters global state each time called
  Function may not return same value for given arguments
    Depends on other parts of global state
    Procedure lower could interact with strlen
Warning:
  Compiler treats procedure call as a black box
  Weak optimizations near them
Remedies:
  Use of inline functions
    GCC does this with –O1
      Within single file
  Do your own code motion
size_t lencnt = 0;
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++; length++;
}
lencnt += length;
return length;
}

## Slide 17: Memory Matters
  Code updates b[i] on every iteration
  Why couldn’t compiler optimize this away?
# sum_rows1 inner loop
.L4:
movsd (%rsi,%rax,8), %xmm0 # FP load
addsd (%rdi), %xmm0 # FP add
movsd %xmm0, (%rsi,%rax,8) # FP store
addq $8, %rdi
cmpq %rcx, %rdi
jne .L4
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}

## Slide 18: Memory Aliasing
  Code updates b[i] on every iteration
  Must consider possibility that these updates will affect program behavior
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
double A[9] =
{ 0, 1, 2,
4, 8, 16},
32, 64, 128};
double B[3] = A+3;
sum_rows1(A, B, 3);
i = 0: [3, 8, 16]
init: [4, 8, 16]
i = 1: [3, 22, 16]
i = 2: [3, 22, 224]
Value of B:

## Slide 19: Removing Aliasing
  No need to store intermediate results
# sum_rows2 inner loop
.L10:
addsd (%rdi), %xmm0 # FP load + add
addq $8, %rdi
cmpq %rax, %rdi
jne .L10
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows2(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
double val = 0;
for (j = 0; j < n; j++)
val += a[i*n + j];
b[i] = val;
}
}

## Slide 20: Optimization Blocker: Memory Aliasing
Aliasing
  Two different memory references specify single location
  Easy to have happen in C
    Since allowed to do address arithmetic
    Direct access to storage structures
  Get in habit of introducing local variables
    Accumulating within loops
    Your way of telling compiler not to check for aliasing

## Slide 21: Exploiting Instruction-Level Parallelism
Need general understanding of modern processor design
  Hardware can execute multiple instructions in parallel
Performance limited by data dependencies
Simple transformations can yield dramatic performance improvement
  Compilers often cannot make these transformations
  Lack of associativity and distributivity in floating-point arithmetic

## Slide 22: Benchmark Example: Data Type for Vectors
/* data structure for vectors */
typedef struct{
size_t len;
data_t *data;
} vec;
/* retrieve vector element
and store at val */
int get_vec_element
(*vec v, size_t idx, data_t *val)
{
if (idx >= v->len)
return 0;
*val = v->data[idx];
return 1;
}
len
data
0
1
len-1
Data Types
  Use different declarations for data_t
  int
  long
  float
  double

## Slide 23: Benchmark Computation
Data Types
  Use different declarations for data_t
  int
  long
  float
  double
Operations
  Use different definitions of OP and IDENT
  + / 0
  * / 1
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements

## Slide 24: Cycles Per Element (CPE)
Convenient way to express performance of program that operates on vectors or lists
Length = n
In our case: CPE = cycles per OP
T = CPE*n + Overhead
  CPE is slope of line
Chart: Elements
| 0 | 193 | 120 | 91 | 95 | 196 | 97 | 181 | 91 | 83 | 43 | 183 | 140 | 146 | 94 | 134 | 163 | 131 | 110 | 182 | 189 | 112 | 141 | 185 | 188 | 47 | 130 | 102 | 59 | 174
psum1 | 2112.6 | 1451.1 | 1188.6 | 1218 | 2131.5 | 1247.4 | 2003.4 | 1190.7 | 1117.2 | 758.1 | 2020.2 | 1629.6 | 1686.3 | 1211.7 | 1568.7 | 1841.7 | 1543.5 | 1358.7 | 2011.8 | 2066.4 | 1373.4 | 1635.9 | 2032.8 | 2058 | 787.5 | 1539.3 | 1285.2 | 905.1 | 1938.3
psum1i | 367.79 | 2107.43 | 1449.43 | 1188.03 | 1224.09 | 2134.47 | 1242.12 | 1999.27 | 1188.03 | 1115.92 | 755.38 | 2017.29 | 1629.7 | 1683.79 | 1215.07 | 1575.62 | 1837.02 | 1548.58 | 1359.29 | 2008.28 | 2071.37 | 1377.32 | 1638.72 | 2035.32 | 2062.36 | 791.43 | 1539.57 | 1287.18 | 899.6 | 1936.17
psum2 | 1535.1 | 1100.4 | 921.9 | 940.8 | 1545.6 | 949.2 | 1455.3 | 917.7 | 865.2 | 623.7 | 1467.9 | 1209.6 | 1253.7 | 936.6 | 1173.9 | 1352.4 | 1150.8 | 1029 | 1461.6 | 1509.9 | 1039.5 | 1215.9 | 1478.4 | 1505.7 | 642.6 | 1152.9 | 987 | 732.9 | 1419.6
psum2i | 367.66 | 1531.11 | 1091.05 | 916.23 | 940.34 | 1549.2 | 952.4 | 1458.77 | 916.23 | 868.01 | 626.87 | 1470.83 | 1211.62 | 1247.79 | 934.32 | 1175.45 | 1350.27 | 1157.36 | 1030.77 | 1464.8 | 1507 | 1042.82 | 1217.64 | 1482.89 | 1500.97 | 650.99 | 1151.33 | 982.54 | 723.33 | 1416.58
psum1
Slope = 9.0
psum2
Slope = 6.0

## Slide 25: Benchmark Performance
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 unoptimized | 22.68 | 20.02 | 19.98 | 20.18
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14

## Slide 26: Basic Optimizations
Move vec_length out of loop
Avoid bounds check on each cycle
Accumulate in temporary
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}

## Slide 27: Effect of Basic Optimizations
Eliminates sources of overhead in loop
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
Combine4 | 1.27 | 3.01 | 3.01 | 5.01

## Slide 28: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 29: Superscalar Processor
Definition: A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction level parallelism that most programs have
Most modern CPUs are superscalar.
Intel: since Pentium (1993)

## Slide 30: Pipelined Functional Units
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2

## Slide 31: Haswell CPU
  8 Total Functional Units
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15

## Slide 32: x86-64 Compilation of Combine4
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 33: Combine4 = Serial Computation (OP = *)
Computation (length=8)
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
Sequential dependence
  Performance: determined by latency of OP
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7

## Slide 34: Loop Unrolling (2x1)
Perform 2x more useful work per iteration
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x OP d[i]) OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}

## Slide 35: Effect of Loop Unrolling
Helps integer add
  Achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 36: Loop Unrolling with Reassociation (2x1a)
Can this change the result of the computation?
Yes, for FP. Why?
void unroll2aa_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x OP (d[i] OP d[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
x = (x OP d[i]) OP d[i+1];
Compare to before

## Slide 37: Effect of Reassociation
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  Why is that? (next slide)
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
2 func. units for FP *
2 func. units for load
4 func. units for int +
2 func. units for load

## Slide 38: Reassociated Computation
What changed:
  Ops in the next iteration can be started early (no dependency)
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);

## Slide 39: Loop Unrolling with Separate Accumulators (2x2)
Different form of reassociation
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}

## Slide 40: Effect of Separate Accumulators
Int + makes use of two load units
2x speedup (over unroll2) for Int *, FP +, FP *
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Unroll 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 41: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/op
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?

## Slide 42: Unrolling & Accumulating
Idea
  Can unroll to any degree L
  Can accumulate K results in parallel
  L must be multiple of K
Limitations
  Diminishing returns
    Cannot go beyond throughput limitations of execution units
  Large overhead for short lengths
    Finish off iterations sequentially

## Slide 43: Unrolling & Accumulating: Double *
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators

## Slide 44: Unrolling & Accumulating: Int +
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 1.00
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Accumulators

## Slide 45: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, unoptimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best | 0.54 | 1.01 | 1.01 | 0.52
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 46: Programming with AVX2
YMM Registers
  16 total, each 32 bytes
  32 single-byte integers
  16 16-bit integers
  8 32-bit integers
  8 single-precision floats
  4 double-precision floats
  1 single-precision float
  1 double-precision float

## Slide 47: SIMD Operations
  SIMD Operations: Single Precision
  SIMD Operations: Double Precision
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
%ymm0
%ymm1
vaddsd %ymm0, %ymm1, %ymm1
+
+
+
+
+
+
+
+

## Slide 48: Using Vector Instructions
Make use of AVX Instructions
  Parallel operations on multiple data elements
  See Web Aside OPT:SIMD on CS:APP web page
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Scalar Best | 0.54 | 1.01 | 1.01 | 0.52
Vector Best | 0.06 | 0.24 | 0.25 | 0.16
Latency Bound | 0.50 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Vec Throughput Bound | 0.06 | 0.12 | 0.25 | 0.12

## Slide 49: What About Branches?
Challenge
  Instruction Control Unit must work well ahead of Execution Unit to generate enough operations to keep EU busy
  When encounters conditional branch, cannot reliably determine where to continue fetching
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
Executing
How to continue?

## Slide 50: Modern CPU Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 51: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
Branch Taken
Branch Not-Taken
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 52: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data
Predict Taken
Begin
Execution
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 53: Branch Prediction Through Loop
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Read invalid location
Executed
Fetched

## Slide 54: Branch Misprediction Invalidation
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Invalidate

## Slide 55: Branch Misprediction Recovery
Performance Cost
  Multiple clock cycles on modern processor
  Can be a major performance limiter
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401036: jmp 401040
. . .
401040: vmovsd %xmm0,(%r12)
i = 99
Definitely not taken
Reload
Pipeline

## Slide 56: Getting High Performance
Good compiler and flags
Don’t do anything stupid
  Watch out for hidden algorithmic inefficiencies
  Write compiler-friendly code
    Watch out for optimization blockers: procedure calls & memory references
  Look carefully at innermost loops (where most work is done)
Tune code for machine
  Exploit instruction-level parallelism
  Avoid unpredictable branches
  Make code cache friendly (Covered later in course)