## Slide 1: Machine-Level Programming II: Control 15-213: Introduction to Computer Systems 6th Lecture, Sep. 17, 2015
Carnegie Mellon
Carnegie Mellon

## Slide 2: Today
Carnegie Mellon
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 3: Processor State (x86-64, Partial)
Carnegie Mellon
Information about currently executing program
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Current stack top
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 4: Condition Codes (Implicit Setting)
Carnegie Mellon
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq instruction

## Slide 5: Condition Codes (Explicit Setting: Compare)
Carnegie Mellon
Explicit Setting by Compare Instruction
  cmpq Src2, Src1
  cmpq b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 6: Condition Codes (Explicit Setting: Test)
Carnegie Mellon
Explicit Setting by Test instruction
  testq Src2, Src1
    testq b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 7: Reading Condition Codes
Carnegie Mellon
SetX Instructions
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 8: x86-64 Integer Registers
%rsp
  Can reference low-order byte
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 9: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
Carnegie Mellon
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to finish job
    32-bit instructions also set upper 32 bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 10: Today
Carnegie Mellon
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 11: Jumping
Carnegie Mellon
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 12: Conditional Branch Example (Old Style)
Carnegie Mellon
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
absdiff:
cmpq %rsi, %rdi # x:y
jle .L4
movq %rdi, %rax
subq %rsi, %rax
ret
.L4: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Generation
  shark> gcc –Og -S –fno-if-conversion control.c
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 13: Expressing with Goto Code
Carnegie Mellon
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
C allows goto statement
Jump to position designated by label
long absdiff_j
(long x, long y)
{
long result;
int ntest = x <= y;
if (ntest) goto Else;
result = x-y;
goto Done;
Else:
result = y-x;
Done:
return result;
}

## Slide 14: General Conditional Expression Translation (Using Branches)
Carnegie Mellon
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
ntest = !Test;
if (ntest) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 15: Using Conditional Moves
Carnegie Mellon
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
result = Then_Expr;
eval = Else_Expr;
nt = !Test;
if (nt) result = eval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC tries to use them
    But, only when known to be safe
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional moves do not require control transfer

## Slide 16: Conditional Move Example
Carnegie Mellon
absdiff:
movq %rdi, %rax # x
subq %rsi, %rax # result = x-y
movq %rsi, %rdx
subq %rdi, %rdx # eval = y-x
cmpq %rsi, %rdi # x:y
cmovle %rdx, %rax # if <=, result = eval
ret
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 17: Bad Cases for Conditional Move
Carnegie Mellon
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 18: Today
Carnegie Mellon
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 19: “Do-While” Loop Example
Carnegie Mellon
C Code
long pcount_do
(unsigned long x) {
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 20: “Do-While” Loop Compilation
Carnegie Mellon
Goto Version
movl $0, %eax # result = 0
.L2: # loop:
movq %rdi, %rdx
andl $1, %edx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
long pcount_goto
(unsigned long x) {
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
Register | Use(s)
%rdi | Argument x
%rax | result

## Slide 21: General “Do-While” Translation
Carnegie Mellon
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 22: General “While” Translation #1
Carnegie Mellon
While version
while (Test)
Body
“Jump-to-middle” translation
Used with -Og
Goto Version
goto test;
loop:
Body
test:
if (Test)
goto loop;
done:

## Slide 23: While Loop Example #1
Carnegie Mellon
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Jump to Middle Version
long pcount_goto_jtm
(unsigned long x) {
long result = 0;
goto test;
loop:
result += x & 0x1;
x >>= 1;
test:
if(x) goto loop;
return result;
}
Compare to do-while version of function
Initial goto starts loop at test

## Slide 24: General “While” Translation #2
Carnegie Mellon
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
“Do-while” conversion
Used with –O1
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 25: While Loop Example #2
Carnegie Mellon
C Code
long pcount_while
(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
Do-While Version
long pcount_goto_dw
(unsigned long x) {
long result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
done:
return result;
}
Compare to do-while version of function
Initial conditional guards entrance to loop

## Slide 26: “For” Loop Form
Carnegie Mellon
for (Init; Test; Update )
Body
General Form
#define WSIZE 8*sizeof(int)
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 27: “For” Loop  While Loop
Carnegie Mellon
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 28: For-While Conversion
Carnegie Mellon
long pcount_for_while
(unsigned long x)
{
size_t i;
long result = 0;
i = 0;
while (i < WSIZE)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
i++;
}
return result;
}
i = 0
i < WSIZE
i++
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
Init
Test
Update
Body

## Slide 29: “For” Loop Do-While Conversion
Carnegie Mellon
C Code
Initial test can be optimized away
long pcount_for
(unsigned long x)
{
size_t i;
long result = 0;
for (i = 0; i < WSIZE; i++)
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
return result;
}
Goto Version
long pcount_for_goto_dw
(unsigned long x) {
size_t i;
long result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned bit =
(x >> i) & 0x1;
result += bit;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 30: Today
Carnegie Mellon
Control: Condition codes
Conditional branches
Loops
Switch Statements

## Slide 31: Switch Statement Example
Carnegie Mellon
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 32: Jump Table Structure
Carnegie Mellon
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
goto *JTab[x];
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Translation (Extended C)
Jump Table
Jump Targets

## Slide 33: Switch Statement Example
Carnegie Mellon
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8
jmp *.L4(,%rdi,8)
What range of values takes default?
Note that w not initialized here
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 34: Switch Statement Example
Carnegie Mellon
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Setup:
switch_eg:
movq %rdx, %rcx
cmpq $6, %rdi # x:6
ja .L8 # Use default
jmp *.L4(,%rdi,8) # goto *JTab[x]

## Slide 35: Assembly Setup Explanation
Carnegie Mellon
Table Structure
  Each target requires 8 bytes
  Base address at .L4
Jumping
  Direct: jmp .L8
  Jump target is denoted by label .L8
  Indirect: jmp *.L4(,%rdi,8)
  Start of jump table: .L4
  Must scale by factor of 8 (addresses are 8 bytes)
  Fetch target from effective Address .L4 + x*8
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6

## Slide 36: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Carnegie Mellon
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}

## Slide 37: Code Blocks (x == 1)
Carnegie Mellon
.L3:
movq %rsi, %rax # y
imulq %rdx, %rax # y*z
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 38: Handling Fall-Through
Carnegie Mellon
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;

## Slide 39: Code Blocks (x == 2, x == 3)
Carnegie Mellon
.L5: # Case 2
movq %rsi, %rax
cqto
idivq %rcx # y/z
jmp .L6 # goto merge
.L9: # Case 3
movl $1, %eax # w = 1
.L6: # merge:
addq %rcx, %rax # w += z
ret
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 40: Code Blocks (x == 5, x == 6, default)
Carnegie Mellon
.L7: # Case 5,6
movl $1, %eax # w = 1
subq %rdx, %rax # w -= z
ret
.L8: # Default:
movl $2, %eax # 2
ret
switch(x) {
. . .
case 5: // .L7
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | Return value

## Slide 41: Summarizing
Carnegie Mellon
C Control
  if-then-else
  do-while
  while, for
  switch
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump (via jump tables)
  Compiler generates code sequence to implement more complex control
Standard Techniques
  Loops converted to do-while or jump-to-middle form
  Large switch statements use jump tables
  Sparse switch statements may use decision trees (if-elseif-elseif-else)

## Slide 42: Summary
Carnegie Mellon
Today
  Control: Condition codes
  Conditional branches & conditional moves
  Loops
  Switch statements
Next Time
  Stack
  Call / return
  Procedure call discipline