## Slide 1: Thread-Level Parallelism 15-213: Introduction to Computer Systems 26th Lecture, Dec. 1, 2015

## Slide 2: Today
Parallel Computing Hardware
  Multicore
    Multiple separate processors on single chip
  Hyperthreading
    Efficient execution of multiple threads on single core
Thread-Level Parallelism
  Splitting program into independent tasks
    Example 1: Parallel summation
  Divide-and conquer parallelism
    Example 2: Parallel quicksort
Consistency Models
  What happens when multiple threads are reading & writing shared state

## Slide 3: Exploiting parallel execution
So far, we’ve used threads to deal with I/O delays
  e.g., one thread per client to prevent one from delaying another
Multi-core/Hyperthreaded CPUs offer another opportunity
  Spread work over threads executing in parallel
  Happens automatically, if many independent tasks
    e.g., running many applications or serving many clients
  Can also write code to make one big task go faster
    by organizing it as multiple parallel sub-tasks

## Slide 4: Typical Multicore Processor
Multiple processors operating with coherent view of memory
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core n-1
…
L3 unified cache
(shared by all cores)
Main memory

## Slide 5: Out-of-Order Processor Structure
Instruction control dynamically converts program into stream of operations
Operations mapped onto functional units to execute in parallel
Functional Units
Int
Arith
Int
Arith
FP
Arith
Load /
Store
Instruction Control
Registers
Instruction Decoder
Op. Queue
Data Cache
Instruction
Cache
PC

## Slide 6: Hyperthreading Implementation
Replicate enough instruction control to process K instruction streams
K copies of all registers
Share functional units
Functional Units
Int
Arith
Int
Arith
FP
Arith
Load /
Store
Instruction Control
Reg B
Instruction Decoder
Op. Queue B
Data Cache
Instruction
Cache
Reg A
Op. Queue A
PC A
PC B

## Slide 7: Benchmark Machine
Get data about machine from /proc/cpuinfo
Shark Machines
  Intel Xeon E5520 @ 2.27 GHz
  Nehalem, ca. 2010
  8 Cores
  Each can do 2x hyperthreading

## Slide 8: Example 1: Parallel Summation
Sum numbers 0, …, n-1
  Should add up to ((n-1)*n)/2
Partition values 1, …, n-1 into t ranges
  n/t values in each range
  Each of t threads processes 1 range
  For simplicity, assume n is a multiple of t
Let’s consider different ways that multiple threads might work on their assigned ranges in parallel

## Slide 9: First attempt: psum-mutex
Simplest approach: Threads sum into a global variable protected by a semaphore mutex.
void *sum_mutex(void *vargp); /* Thread routine */
/* Global shared variables */
long gsum = 0; /* Global sum */
long nelems_per_thread; /* Number of elements to sum */
sem_t mutex; /* Mutex to protect global sum */
int main(int argc, char **argv)
{
long i, nelems, log_nelems, nthreads, myid[MAXTHREADS];
pthread_t tid[MAXTHREADS];
/* Get input arguments */
nthreads = atoi(argv[1]);
log_nelems = atoi(argv[2]);
nelems = (1L << log_nelems);
nelems_per_thread = nelems / nthreads;
sem_init(&mutex, 0, 1);
psum-mutex.c

## Slide 10: psum-mutex (cont)
/* Create peer threads and wait for them to finish */
for (i = 0; i < nthreads; i++) {
myid[i] = i;
Pthread_create(&tid[i], NULL, sum_mutex, &myid[i]);
}
for (i = 0; i < nthreads; i++)
Pthread_join(tid[i], NULL);
/* Check final answer */
if (gsum != (nelems * (nelems-1))/2)
printf("Error: result=%ld\n", gsum);
exit(0);
}
psum-mutex.c
Simplest approach: Threads sum into a global variable protected by a semaphore mutex.

## Slide 11: psum-mutex Thread Routine
Simplest approach: Threads sum into a global variable protected by a semaphore mutex.
/* Thread routine for psum-mutex.c */
void *sum_mutex(void *vargp)
{
long myid = *((long *)vargp); /* Extract thread ID */
long start = myid * nelems_per_thread; /* Start element index */
long end = start + nelems_per_thread; /* End element index */
long i;
for (i = start; i < end; i++) {
P(&mutex);
gsum += i;
V(&mutex);
}
return NULL;
}
psum-mutex.c

## Slide 12: psum-mutex Performance
Shark machine with 8 cores, n=231
Threads (Cores) | 1 (1) | 2 (2) | 4 (4) | 8 (8) | 16 (8)
psum-mutex (secs) | 51 | 456 | 790 | 536 | 681
Nasty surprise:
  Single thread is very slow
  Gets slower as we use more cores

## Slide 13: Next Attempt: psum-array
Peer thread i sums into global array element psum[i]
Main waits for theads to finish, then sums elements of psum
Eliminates need for mutex synchronization
/* Thread routine for psum-array.c */
void *sum_array(void *vargp)
{
long myid = *((long *)vargp); /* Extract thread ID */
long start = myid * nelems_per_thread; /* Start element index */
long end = start + nelems_per_thread; /* End element index */
long i;
for (i = start; i < end; i++) {
psum[myid] += i;
}
return NULL;
}
psum-array.c

## Slide 14: psum-array Performance
Orders of magnitude faster than psum-mutex
Chart: Parallel Summation
| 1(1) | 2(2) | 4(4) | 8(8) | 16(8)
psum-array | 5.36 | 4.24 | 2.54 | 1.64 | 0.94

## Slide 15: Next Attempt: psum-local
Reduce memory references by having peer thread i sum into a local variable (register)
/* Thread routine for psum-local.c */
void *sum_local(void *vargp)
{
long myid = *((long *)vargp); /* Extract thread ID */
long start = myid * nelems_per_thread; /* Start element index */
long end = start + nelems_per_thread; /* End element index */
long i, sum = 0;
for (i = start; i < end; i++) {
sum += i;
}
psum[myid] = sum;
return NULL;
}
psum-local.c

## Slide 16: psum-local Performance
Significantly faster than psum-array
Chart: Parallel Summation
| 1(1) | 2(2) | 4(4) | 8(8) | 16(8)
psum-array | 5.36 | 4.24 | 2.54 | 1.64 | 0.94
psum-local | 1.98 | 1.14 | 0.6 | 0.32 | 0.33

## Slide 17: Characterizing Parallel Program Performance
p processor cores, Tk is the running time using k cores
Def. Speedup: Sp = T1 / Tp
  Sp is relative speedup if T1 is running time of parallel version of the code running on 1 core.
  Sp is absolute speedup if T1 is running time of sequential version of code running on 1 core.
  Absolute speedup is a much truer measure of the benefits of parallelism.
Def. Efficiency: Ep = Sp /p = T1 /(pTp)
  Reported as a percentage in the range (0, 100].
  Measures the overhead due to parallelization

## Slide 18: Performance of psum-local
Threads (t) | 1 | 2 | 4 | 8 | 16
Cores (p) | 1 | 2 | 4 | 8 | 8
Running time (Tp) | 1.98 | 1.14 | 0.60 | 0.32 | 0.33
Speedup (Sp) | 1 | 1.74 | 3.30 | 6.19 | 6.00
Efficiency (Ep) | 100% | 87% | 82% | 77% | 75%
Efficiencies OK, not great
Our example is easily parallelizable
Real codes are often much harder to parallelize
  e.g., parallel quicksort later in this lecture

## Slide 19: Amdahl’s Law
  Gene Amdahl (Nov. 16, 1922 – Nov. 10, 2015)
Captures the difficulty of using parallelism to speed things up.
Overall problem
  T Total sequential time required
  p Fraction of total that can be sped up (0  p  1)
  k Speedup factor
Resulting Performance
  Tk = pT/k + (1-p)T
    Portion which can be sped up runs k times faster
    Portion which cannot be sped up stays the same
  Least possible running time:
    k = 
    T = (1-p)T

## Slide 20: Amdahl’s Law Example
Overall problem
  T = 10 Total time required
  p = 0.9 Fraction of total which can be sped up
  k = 9 Speedup factor
Resulting Performance
  T9 = 0.9 * 10/9 + 0.1 * 10 = 1.0 + 1.0 = 2.0
  Least possible running time:
    T = 0.1 * 10.0 = 1.0

## Slide 21: A More Substantial Example: Sort
Sort set of N random numbers
Multiple possible algorithms
  Use parallel version of quicksort
Sequential quicksort of set of values X
  Choose “pivot” p from X
  Rearrange X into
    L: Values  p
    R: Values  p
  Recursively sort L to get L
  Recursively sort R to get R
  Return L : p : R

## Slide 22: Sequential Quicksort Visualized
X
p
L
p
R
p2
L2
R2
p2



L

## Slide 23: Sequential Quicksort Visualized
X
p
R
p3
L3
R3
p3
L



R
p
L
R

## Slide 24: Sequential Quicksort Code
Sort nele elements starting at base
  Recursively sort L or R if has more than one element
void qsort_serial(data_t *base, size_t nele) {
if (nele <= 1)
return;
if (nele == 2) {
if (base[0] > base[1])
swap(base, base+1);
return;
}
/* Partition returns index of pivot */
size_t m = partition(base, nele);
if (m > 1)
qsort_serial(base, m);
if (nele-1 > m+1)
qsort_serial(base+m+1, nele-m-1);
}

## Slide 25: Parallel Quicksort
Parallel quicksort of set of values X
  If N  Nthresh, do sequential quicksort
  Else
    Choose “pivot” p from X
    Rearrange X into
      L: Values  p
      R: Values  p
    Recursively spawn separate threads
      Sort L to get L
      Sort R to get R
    Return L : p : R

## Slide 26: Parallel Quicksort Visualized
X
p
L
p
R
p2
p3
p2
L2
R2
L3
R3
p3
p



L



R
p

## Slide 27: Thread Structure: Sorting Tasks
Task: Sort subrange of data
  Specify as:
    base: Starting address
    nele: Number of elements in subrange
Run as separate thread
X
  
Task Threads

## Slide 28: Small Sort Task Operation
Sort subrange using serial quicksort
X
  
Task Threads

## Slide 29: Large Sort Task Operation
X
  
p
L
R
X
  
p
L
R
Partition Subrange
Spawn 2 tasks

## Slide 30: Top-Level Function (Simplified)
Sets up data structures
Calls recursive sort routine
Keeps joining threads until none left
Frees data structures
void tqsort(data_t *base, size_t nele) {
init_task(nele);
global_base = base;
global_end = global_base + nele - 1;
task_queue_ptr tq = new_task_queue();
tqsort_helper(base, nele, tq);
join_tasks(tq);
free_task_queue(tq);
}

## Slide 31: Recursive sort routine (Simplified)
Small partition: Sort serially
Large partition: Spawn new sort task
/* Multi-threaded quicksort */
static void tqsort_helper(data_t *base, size_t nele,
task_queue_ptr tq) {
if (nele <= nele_max_sort_serial) {
/* Use sequential sort */
qsort_serial(base, nele);
return;
}
sort_task_t *t = new_task(base, nele, tq);
spawn_task(tq, sort_thread, (void *) t);
}

## Slide 32: Sort task thread (Simplified)
Get task parameters
Perform partitioning step
Call recursive sort routine on each partition
/* Thread routine for many-threaded quicksort */
static void *sort_thread(void *vargp) {
sort_task_t *t = (sort_task_t *) vargp;
data_t *base = t->base;
size_t nele = t->nele;
task_queue_ptr tq = t->tq;
free(vargp);
size_t m = partition(base, nele);
if (m > 1)
tqsort_helper(base, m, tq);
if (nele-1 > m+1)
tqsort_helper(base+m+1, nele-m-1, tq);
return NULL;
}

## Slide 33: Parallel Quicksort Performance
Serial fraction: Fraction of input at which do serial sort
Sort 227 (134,217,728) random values
Best speedup = 6.84X

## Slide 34: Parallel Quicksort Performance
Good performance over wide range of fraction values
  F too small: Not enough parallelism
  F too large: Thread overhead + run out of thread memory

## Slide 35: Amdahl’s Law & Parallel Quicksort
Sequential bottleneck
  Top-level partition: No speedup
  Second level:  2X speedup
  kth level:  2k-1X speedup
Implications
  Good performance for small-scale parallelism
  Would need to parallelize partitioning step to get large-scale parallelism
    Parallel Sorting by Regular Sampling
      H. Shi & J. Schaeffer, J. Parallel & Distributed Computing, 1992

## Slide 36: Parallelizing Partitioning Step
p
L1
R1
X1
X2
X3
X4
L2
R2
L3
R3
L4
R4
Parallel partitioning based on global p
L1
R1
L2
R2
L3
R3
L4
R4
Reassemble into partitions

## Slide 37: Experience with Parallel Partitioning
Could not obtain speedup
Speculate: Too much data copying
  Could not do everything within source array
  Set up temporary space for reassembling partition

## Slide 38: Lessons Learned
Must have parallelization strategy
  Partition into K independent parts
  Divide-and-conquer
Inner loops must be synchronization free
  Synchronization operations very expensive
Beware of Amdahl’s Law
  Serial code can become bottleneck
You can do it!
  Achieving modest levels of parallelism is not difficult
  Set up experimental framework and test multiple strategies

## Slide 39: Memory Consistency
What are the possible values printed?
  Depends on memory consistency model
  Abstract model of how hardware handles concurrent accesses
Sequential consistency
  Overall effect consistent with each individual thread
  Otherwise, arbitrary interleaving
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Wa
Rb
Wb
Ra
Thread consistency
constraints

## Slide 40: Sequential Consistency Example
Impossible outputs
  100, 1 and 1, 100
  Would require reaching both Ra and Rb before Wa and Wb
Wa
Rb
Wb
Ra
Wb
Rb
Ra
Ra
Rb
Wb
Ra
Wa
Rb
Wa
Ra
Rb
Rb
Ra
100, 2
200, 2
2, 200
1, 200
2, 200
200, 2
Wa
Rb
Wb
Ra
Thread consistency
constraints
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 41: Non-Coherent Cache Scenario
Write-back caches, without coordination between them
Main Memory
a:1
b:100
Thread1 Cache
a: 2
Thread2 Cache
b:200
a:1
print 1
b:100
print 100
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 42: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 43: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
print 200
b:200
S
b:200
S
print 2
a:2
S
a: 2
S
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
When cache sees request for one of its E-tagged blocks
  Supply value from cache
  Set tag to S